## Slide 1: Admin Throttle
Design

## Slide 2
1 2 3 4 5 6 7 . . . to 100
1234567890123456789012345678901234567890123456789012345678901234567890123456789. . .
01 Train PhyAdr/Slot VirAdr/Slot State Speed Dir Light Bell Horn Mute Location
02 ----- ----------- ----------- ----- ----- --- ----- ---- ---- ---- --------
03 1 3333 / 3 13 / 10 W 60 F on off off off 13 14 26
04 2 2222 / 2 14 / 11 BH 0 R on on on on 103 104 77
05 -
06 -
07
08 Last msg received: set speed train 2 to 50
09 bytes in decimal / bytes in hex
10 Switches Commands
11 0 1 2 3 4 5 6 7 8 9 Xf read XML Za s#…s# initialize loco
12 0 T T T T T T C C T SEa select loco STa steal loco
13 1 C * T C T C C T C *
14 2 T T C C C C C Cs close Ts throw
15 Vt n -- set velocity of t to n
16 Ft forward Rt reverse Q quit
17 Bt bell Ht horn . halt all
18 Lt light Mt mute
19 P+ power on P- power off
20 a = physical loco address s = switch s# = sensor#
21 t = train f = file name n = 0..127
22 Error messages displayed here
23 >
Switch commands use the switch number
It: increases the speed of train t by 30, to a limit of 127
Dt: decreases the speed of train t by 30, to a limit of 0
Train data
In PydaRail mode ,this represents data sent by PydaRail to all Othrottles. I need to add some messages for this.
In Standalone mode, as indicated by user
Switches
In Pydarail mode, this represents data sent by PydaRail.
In Standalone mode, as reported by the railroad
Admin Throttle
What messages are heard by this throttle
In PydaRail mode
  Only the messages that PydaRail sends to throttles.
In Standalone mode with the simulator
  Commands from all other throttles
  Sensor and switch reports
In Standalone mode with the LocoBuffer
  Commands from the Digiitrax throttles
  Sensor and switch reports
Mode
Initially in stand alone mode
In response to Xf (read XML) goes into PydaRail mode
Train states
M moving
H halt
BH begin halt
W wait
BW begin wait
BD begin change direction
E error
U unknown
TCP/IP connection
Default IP 127.0.0.1 Port 14804
If server not found, then asks

## Slide 3
RailroadBig
(tcp/ip)
Screen
Keyboard
Keyboard Task
Railroad Task
Screen Manager
Railroad Manager
Server Socket
ClientSocket

## Slide 4
RailroadBig
(tcp/ip)
Screen
Keyboard
Keyboard Task
Railroad Task
Screen Manager
Railroad Manager
Server Socket
ClientSocket
2a. ReceiveMessage (SockId, 0, 0) : size
2b. ReadByte(0) : byte
1a. ClearBuffer(0)
1b. WriteByte(byte, 0)
1c. SendMessage (SockId, Ip, Port, 0) : flag
3. Put (message)
4. Put various updates
Message
railroad Ada program
 screen
5a. MoveCursor(column, row)
5b. Put (string)
39DLL

## Slide 5
RailroadBig
(tcp/ip)
Screen
Keyboard
Keyboard Task
Railroad Task
Screen Manager
Railroad Manager
Server Socket
ClientSocket
6a. ReceiveMessage (SockId, 0, 0) : Size
6b. ReadByte(0) : Byte
Message
keyboard Ada program
 railroad
3a. MoveCursor(column, row)
3b. Put (string)
1. Get :Command
4. SendMessage (Command)
5a. ClearBuffer(0)
5b. WriteByte(Byte, 0)
5c. SendMessage (SockId, Ip, Port, 0) : Flag
2a. PutError (String)
2b. PutPrompt(String)
39DLL

## Slide 6
RailroadBig
(tcp/ip)
Screen
Keyboard
Keyboard Task
Railroad Task
Screen Manager
Railroad Manager
Server Socket
ClientSocket
6. ReceiveMessage SL_RD_DATA
4. ReceiveMessage LOCO_ADR
5. SendMessage SL_RD_DATA
9. ReceiveMessage MOVE_SLOTS
7. Put (SL_RD_DATA )
10. Put (slot#)
Selecting or stealing a loco address (assuming no errors)
11a. MoveCursor(column, row)
11b. Put (string)
1. Get (Rn)
3. SendMessage LOCO_ADR
8. SendMessage MOVE_SLOTS
39DLL
2. sendMessage(SL or SE)
1’a. PutError (String)
1’b. PutPrompt(String)

## Slide 7
Packages
Globals.ads
+ kNumTrains := 4
+ kNumSwitches := 26
+ kMaxLenMsg := 14
+ kMaxLenError := 80
+ kGreen := “green”
+ kWhite := “white”
+ kRed := “red”
+ kYellow := “yellow”
+ kNoColor := “ “
+ kDeltaSpeed := 10
+ ColorType string(1..6)
+ LocoAddressType (0..4444)
+ SlotType (0..120)
+ DirectionType (Forward, Backward)
+ SpeedType (0..127)
+ OnOffType (On, Off)
+ TrainType record of
isConnected,
phyadr, physlot, viradr, virslot, state, direction,
speed, light, horn, bell, mute, sensors(a list of natural)
+ TrainArrayType (1..kNumTrains) of TrainType
+ SwitchType (Closed, Thrown, Moving, Unknown)
+ SwitchArrayType (1..kNumSwitches) of SwitchType
+ ByteArrayType array (Integer RANGE <>) of unsigned_8
+ MessageType bytes(1..kMaxLenMsg), InUse
+ CmdType (ReadXML, InitializeLoco, SelectLoco, StealLoco, Close, Throw, Forward, Backward,
Increase, Decrease, Halt, Horn, Bell, Mute, Light, Power, MoveSlots, Unknown, Quit)
+ CommandType record of cmd, natural

## Slide 8
Globals.ads
+ ConnectSocket C.Double;
+ IpStrAda String := "127.0.0.1";
+ IpStrC Chars_Ptr := New_String(IpStrAda);
+ CEmptyString Chars_Ptr := New_String("");
+ ServerPort c.double := c.double(14804);
+ Buffer0 C.Double := C.Double(0.0);
+ BlockingMode C.double := c.double(0);
+ NonblockingMode C.double := c.double(1);
+ CValue C.Double;
+ CZero C.double := c.double(0);

## Slide 9
Packages
Api39dll
+f dllInit
+f TcpConnect
+f ClearBuffer
+f WriteByte
+f SendMessage
+f ReceiveMessage
+f ReadByte
Screen
+d ScreenDepth
+d ScreenWidth
+p Beep
+p ClearScreen
+p MoveCursor
ScreenManager
+p Initialize
+p PutTrains(Trains)
+p PutMessage(Stgring)
+p PutSwitches(Switches)
+p PutError(String)
+p PutPrompt(String)
+o objScreenManager
RailroadTask
+e Start
+o obj RailroadTask
RailroadManager
-d Trains
-d Switches
-d Last message received
+p Initialize
+p Put(Message)
+f GetMessage(Command, Success):Message
+o objRailroadManager
AdminThrottle
It all starts here
Connect to server
Start tasks
Initialize managers
KeyboardTask
+e Start
+o objKeyboardTask

## Slide 10
At startup
Trains initialized to slot number for a train is 0 until registered direction forward, speed 0 light, horn, bell, mute all off
Message sent to throw all switches
Last message received is blank

## Slide 11
-- Constants for direction, lights, horn, bell, mute, turnout action
kForward := 16#00#;
kBackward := 16#20#; -- 0010 0000
kLightsOn := 16#10#; -- 0001 0000
kLightsOff := 16#00#;
kHornOn := 16#02#; -- 0000 0010
kHornOff := 16#00#;
kBellOn := 16#01#; -- 0000 0001
kBellOff := 16#00#;
kMuteOn := 16#08#; -- 0000 1000
kMuteOff := 16#00#;
-- Constants for switches
kCloseIt := 16#20#; -- 0010 0000
kIsClosed := 16#10#; -- 0001 0000
kThrown := 16#00#; -- 0000 0000
-- Opcodes
OPC_GPON := 16#83#; -- power on
OPC_GPOFF := 16#82#; -- power off
OPC_INPUT_REP := 16#B2#; -– report sensor fired
OPC_SW_REP := 16#B1#; -– report turnout now open/thrown
OPC_LOCO_SPD := 16#A0#; -- set speed
OPC_LOCO_DIRF := 16#A1#; -- set direction, horn, bell, lights
OPC_LOCO_SND := 16#A2#; -- set mute and unmute sound
OPC_SW_REQ := 16#B0#; -- move a turnout
OPC_LOCO_ADR := 16#BF#; -- request for slot data
OPC_SL_RD_DATA := 16#E7#; -- slot data response
OPC_LONG_ACK := 16#B4#; -- insufficient slots
OPC_MOVE_SLOTS := 16#BA#; -- register slot
All the above are declared as “constant unsigned_8”

## Slide 12
Messages Sent
OPC_SW_REQ – move switch
<0xB0><SW1><SW2><CHK>
byte1 := switch number (0..127)
byte2 := switch direction
OPC_LOCO_SPD – set speed
<0x A0 ><SLOT#><SPEED><CHK>
byte1 := slot;
byte2 := speed
OPC_LOCO_DIRF – set direction, lights, horn, bell
<0xA1><SLOT#><DIR_STATE><CHK>
byte1 := slot;
byte2 := 16#00# or Direction or Light or Horn or Bell;
OPC_LOCO_SND – set mute
<0xA2><SLOT#><SOUND><CHK>
byte1 := slot;
byte2 := 16#00# | Mute;
OPC_LOCO_ADR – request information about a loco address
<0xBF><adrhigh><adrlow><chk>
byte2 := 16#FF# and (LocoAddress mod 128);
byte1 := 16#FF# and ((LocoAddress - byte2) / 128);
OPC_MOVE_SLOTS – register a slot
<0xBA><slot#><slot#><chk>
byte1 := slot;
byte2 := slot;
checksum := 16#FF# xor opCode xor byte1 xor byte2;
clearbuffer();
writebyte(opCode);
writebyte(byte1);
writebyte(byte2);
writebyte(checksum);
sendmessage(socketToSimulator);

## Slide 13
Messages Received
All the output messages, which are displayed on the screen, but otherwise ignored.
OPC_INPUT_REP – report sensor fired
<0xB2><SN1><SN2><CHK>
SN1 <0,A6,A5,A4,A3,A2,A1,A0>
SN2 <0,X,I,L,A10,A9,A8,A7>
I = 1 => add 1000 to the address
L = 1 => sensor high else low
OPC_SW_REP – report turnout now open/thrown
<0xB1><SW1><SW2><CHK>
SW1 <0,A6,A5,A4,A3,A2,A1,A0>
SW2 <0,1,I,L,A10,A9,A8,A7>
I = 1 => turnout closed else thrown
OPC_SL_RD_DATA – report loco address information
<0xE7><0E><slot#><status><adrlow><spd><dirf><trk><ss2><adrhigh><snd><id1><id2><chk>
0 1 2 3 4 5 6 7 8 9 10 11 12 13
slot# the number of the slot
status address already registered in the indicated slot (D5D4 == 11) or
    the slot is available for registering the address (D5D4 == other)
  (The simulator makes no attempt to get the other bits correct and
  sets them all to 0's.)
address that was sent
other information that we choose to ignore so we set it to 0x00;
OPC_LONG_ACK – report that there aren’t enough slots
<0xB4><lopc><ack1><chk>
lopc 0x00, indicating insufficient slots
other information that we choose to ignore so the simulator sets it to 0x00;